## Slide 1
Seamless VoWLAN Handoff Management based on Estimation of AP Queue Length & Frame Retries
Muhammad Niswar
Graduate School of Information Science
Nara Institute of Science & Technology
JAPAN
<number>
Notes: <number>
<number>

## Slide 2
Outline
Background
VoWLAN Challenges
Existing Handoff Schemes
Objectives
Proposed Handoff Decision Metrics
Evaluation of Proposed Handoff Decision Metrics
Proposed Handoff Strategy
Evaluation of Proposed Handoff Strategy
Conclusion
<number>
Notes: <number>
<number>

## Slide 3
Background
Huge demand for Voice over IP (VoIP) service over WLANs
Dominant WLAN today: IEEE802.11
Mobile Node (MN) more likely to traverse several hotspots during VoIP call
Need reliable Handoff Management for real-time applications such as VoIP
AP2
AP1
MN
AP3
<number>
Notes: <number>
<number>

## Slide 4
VoIP over WLAN (VoWLAN) Challenges (1)
  VoIP sensitive to delay and packet loss
  IEEE802.11-based WLAN not originally designed to support delay & packet loss sensitive applications
  Physical characteristics of wireless much worse than wired lines
<number>
Notes: <number>

## Slide 5
VoIP over WLAN (VoWLAN) Challenges (2)
VoIP quality mainly degraded due to
  Poor Wireless Link Quality
    movement, radio interference and obstacles
  Congestion at AP
    Increase number of Mobile Terminals
MN need to detect degradation of VoIP quality & handoff to another WLAN
Require Handoff Management to maintain VoIP quality during handoff
<number>
Notes: <number>

## Slide 6
Existing Handoff Management
Network Layer
  Mobile IP
  FMIPv6
  HMIPv6
Transport Layer
  M-TCP
  M-UDP
  M-SCTP
<number>
Notes: <number>

## Slide 7
Limitation of Existing Handoff Management
Handoff decision metric and criteria are not discussed in detail
Rely on only upper layer information
  Packet loss
  Delay
  MOS
<number>
Notes: <number>

## Slide 8
Selecting Handoff Decision Metric
Common Handoff Decision Metric
  Received Signal Strength
  Delay
  Packet Loss
Handoff Decision Metric from Layer 2
  Information of MAC layer has potential to be significant metric
  Frame retries inevitably occur before packet loss allows an MN to detect wireless link condition quickly
<number>
Notes: <number>

## Slide 9
Objectives
Propose reliable Handoff Decision Metrics
Develop Mobile Terminal-based Handoff Management to maintain VoIP call quality during handoff
<number>
Notes: <number>
<number>

## Slide 10
Proposed Handoff Decision Metrics
Retransmission of Request-To-Send (RTS) Frame
  Metric for indicating wireless link condition
AP Queue Length
  Metric for indicating congestion state at AP
<number>
Notes: <number>

## Slide 11
Proposed Handoff Decision Metrics: Request To Send (RTS) Retries
To prevent collision in wireless network due to hidden node
To clear out area
RTS Retries can indicate condition of wireless link
RTS
CTS
Frame
ACK
MN
AP
<number>
Notes: <number>
<number>

## Slide 12
Proposed Handoff Decision Metrics: Why RTS Frame Retries?
Current WLANs employ multi-rate function
  Dynamically change transmission rate
RTS frame always transmitted at lowest rate (6 Mb/s)‏
  MN can properly detect wireless link condition in fixed transmission rate
<number>
Notes: <number>

## Slide 13
Proposed Handoff Decision Metrics: AP Queue Length
With increase of MNs in WLAN, packets queued in AP buffer also increase
Current widely deployed IEEE802.11(a/b/g) standard does not provide mechanism to report AP Queue Length Status
  Estimated from MN
<number>
Notes: <number>
<number>

## Slide 14
Proposed Handoff Decision Metrics: Estimating AP Queue Length using ICMP message
MN
AP
RTS
RTS
CTS
CTS
ACK
ICMP (Probe Reply)‏
ICMP (Probe Request)‏
ACK
RTT
Queuing Delay
<number>
Notes: <number>
<number>

## Slide 15
Simulation Experiment
To evaluate performance of proposed Handoff Decision Metrics and Handoff Strategy
Simulation Tools:
  Qualnet 4.0.1
<number>
Notes: <number>
<number>

## Slide 16
Simulation Parameters
VoIP Codec
G.711
WLAN Standard
IEEE 802.11g
Supported Data Rate
6, 9, 12, 18, 24, 36, 48, 54Mbps
Fading Model
Nakagami Ricean K = 4.84
SIFS
16 us
Slot Time
9 us
CW min, CWmax
15, 1023
<number>
Notes: <number>

## Slide 17
Assessment of VoIP Quality
Mean Opinion Score (MOS)‏
  E-model standardized by ITU-T
  Determined based on R-factor
  R = 94.2 - Id – Ie
  MOS > 3.6 indicates adequate VoIP call quality
R-factor
MOS
User Experience
90
4.3
Excellent
80
4.0
Good
70
3.6
Fair
60
3.1
Poor
50
2.6
Bad
<number>
Notes: <number>
<number>

## Slide 18
Evaluation of Proposed Handoff Metric (RTS Retries): Simulation Model & Result for RTS Retries
AP
Router
CN
MN
VoIP (G.711)‏
Packet Size = 160 bytes
Interval = 20 ms
MN speed = 1 m/s
R_thr = 0.6
<number>
Notes: <number>
<number>

## Slide 19
Evaluation of Proposed Handoff Metric (AP Queue Length): Simulation Result for AP Queue Length
AP
Router
CN
:
:
….
VoIP (G.711)‏
Packet Size = 160 bytes
Interval = 20 ms
<number>
Notes: <number>
<number>

## Slide 20
Evaluation of Proposed Handoff Metric (AP Queue Length): Relationship among AP Queue Length, RTT & MOS
AP
Router
CN
:
:
….
VoIP (G.711)‏
Packet Size = 160 bytes
Interval = 20 ms
RTT_thr = 200 ms
<number>
Notes: <number>
<number>

## Slide 21
Evaluation of Handoff Decision Metric Simulation Results
To satisfy adequate VoIP calls
  RTS retry ratio < 0.6
  RTT < 200 ms
<number>
Notes: <number>

## Slide 22
Proposed Handover Strategy
Multi-homed MN
Handoff manager (HM) on transport layer to control handoffs
Employ RTS retries & ICMP message to estimate of AP Queue length (RTT) as handoff decision metrics
Employ Single-Path & Multi-Path Transmission to support Soft-Handoff
CN
AP1
AP2
MN
<number>
Notes: <number>
<number>

## Slide 23
Proposed Handoff Strategy: Switching of Single Path/Multi-Path Transmission
Single Path
AP1RTT<RTT_thr
&
AP2RTT<RTT_thr
Yes
No
AP1RTT >AP2RTT
AP1RTT < AP2RTT
No
No
Yes
Yes
IF_Retry > R_Sthr
Yes
Multi Path
Single Path to IF2
Single Path to IF1
IF_Retry > R_Sthr
Yes
Multi Path
No
No
Multi Path
AP1RTT < RTT_thr
&
AP2RTT < RTT_thr
AP1RTT > AP2RTT
AP1RTT < AP2RTT
No
Yes
Comparing Retry Ratio
No
No
Comparing Retry Ratio
Single Path to IF2
Single Path to IF1
Yes
Yes
<number>
Notes: <number>
<number>

## Slide 24
Proposed Handoff Strategy: Comparing Retry Ratio
IF1_Retry :IF2_Retry
>
<
=
Multi Path
IF1_Retry
< R_Mthr
Comparing Retry Ratio
IF2_Retry
< R_Mthr
Multi Path
Multi Path
Single Path to IF2
Single Path to IF1
Yes
Yes
No
No
<number>
Notes: <number>
<number>

## Slide 25
Proposed Handoff Strategy: Avoiding Ping-Pong Effect
When traffic load in WLAN abruptly increases, all MNs employ RTT information as HO decision criterion
All MNs simultaneously handoff to neighbor AP
Neighbor AP suddenly congested and all MNs switch back to previous AP
Leads to ping-pong effect
Solution:
  MN with lowest transmission rate executes HO first followed by next lowest transmission
<number>
Notes: <number>
<number>

## Slide 26
Proposed Handoff Strategy: Avoiding Ping-Pong Effect
Calculate RTT
RTT > RTT_thr
Handover to another AP
ARF_thr=0
ARF_thr++
No
ARF_thr=0 6Mbps
ARF_thr=1 9Mbps
ARF_thr=2 12Mbps
ARF_thr=3 18Mbps
ARF_thr=4 24Mbps
ARF_thr=5 36Mbps
ARF_thr=6 48Mbps
ARF_thr=7 54Mbps
CurrTime‐LastTime
> Time_thr
Yes
Transmission Rate ≤ ARF_thr
Yes
Yes
No
No
LastTime = CurrTime
Yes
<number>
6M
6M
12M
54M
12M
Notes: <number>

## Slide 27
Proposed Handoff Strategy: Elimination of Redundant Probe Packets
Every MN measures RTT using probe packets
Packets produce redundant traffic leading to unnecessary network overload
Solution:
  Only one MN sends probe packets
  Rest of MNs measure RTT by capturing existing probe packets over wireless link
<number>
Notes: <number>
<number>

## Slide 28
Proposed Handoff Strategy: Elimination of Redundant Probe Packets
<number>
Captured Packet
probe packet size ==
captured packet size
ProbeLastTime=CurrTime
Probe Reply?
(Source MAC Addr = =AP’s Addr)
probeReply_Time=CurrTime
probeReq_Time=CurrTime
W-RTT=
probeReply_Time－probeReq_Time
Yes
No
Yes
No
Notes: <number>

## Slide 29
Evaluation of Proposed Handoff Strategy Simulation Scenarios
Proposed Handoff Strategy vs. Handoff Strategy based on Data Frame Retries
MNs establish VoIP call with their CNs
15 MNs randomly move between two APs
AP1
AP2
Router
CN
:
:
100m
VoIP (G.711)‏
Packet Size = 160 bytes
Interval = 20 ms
MN speed = 1 m/s
<number>
Notes: <number>

## Slide 30
Evaluation of Proposed Handoff Strategy: Simulation Results
Proposed Handoff Strategy
Handoff Strategy based on
Data Frame Retries
<number>
AP Queue Length
MOS
Average MOS: 1.80
Average MOS: 3.60
Notes: <number>
<number>

## Slide 31
Conclusion
Proposed Handoff Decision Metrics
  RTS Retries
  Estimation of AP Queue Length (RTT)
Proposed Handoff strategy for VoIP application
  Execute Handoff based on wireless link condition & congestion state at AP
  Able to detect congested AP, not to execute Handoff to congested AP
Contributions:
  Seamless Handover
  Load-balancing between APs
<number>
Notes: <number>
<number>

## Slide 32
Thank You
<number>
Notes: <number>
<number>