Package II
Laboratory Equipment
Control Systems and Instrumentation Laboratory

No.	Item and Specifications	Units	Main Preference	Alternatives
1/5	Level/Flow Process Control Training Systems (PCTS)	1 package	SYNTEK WLF 922 Malaysia	NO ALTERNATIVE
2/5	Fluid/Water Process Control Demonstration Units or Trainers Kit (combined or seperated) including: / * Level Process Control / * Flow Process Control / * Temperature Process Control / Moveable on wheeled table or trolley top units, around 100 kg/unit / Including: / Industrial Standard I/O Analog and Digital Interface units / Sensors (level, flow, temperatures) for Visual Observation/Manual Measurements / Sensors/Transmitters (level, flow, temperatures) for Data Aquisition and Computer Control / Manual and Automatic (electromagnetic) Valves and other actuaters / Pumps (+/- 1 liter/sec, 5 m head), Heaters, thermostats and Heat Exchangers (for Temperature Process Control), temperature ranges: 0 -100 Celcius / Serial Comm Data I/O Ports for external computer connection and control (drivers and software included, if necessary) / Storage tanks for +/- 15 litres of water capacity / Internal Control Systems (PID, Digital Controllers, PLC) is optional, not required / Control Softwares are optional, not required	1 combined experimental units, or 2 or 3 seperated units (self-contained)	FEEDBACK 38-003 System / United Kingdom	1. GUNT RT 5XX/6XX series, GERMANY / 2. EDIBON UCP series, SPAIN

No.	Item and Specifications	Units	Main Preference	Alternatives
3/5	Gas/Air Process Control Demonstration Units or Trainers Kit (combined or seperated) including: / * Temperature Process Control / * Pressure Process Control / Moveable on wheeled table top or trolley top units, around 100 kg/unit / Including: / Industrial Standard I/O Analog and Digital Interface units / Sensors (pressure and temperatures) for Visual Observation/Manual Measurements / Sensors/Transducers/Transmitters (pressure and temperatures) for Data Aquisition and Computer Control / Manual and Automatic (electromagnetic) Valves and other actuaters / Compressors, Heaters/Coolers, thermostats and Heat Exchangers (for Temperature Process Control), temperature ranges: 0-100 Celcius / Serial Comm Data I/O Ports for external computer connection and control (drivers and software included, if necessary) / Storage tanks for +/- 15 litres of water capacity / Internal Control Systems (PID, Digital Controllers, PLC) is optional, not required / Control Softwares are optional, not required	1 combined experimental units, or 2 seperated units / (self-contained)	FEEDBACK 38-004 and 37-100 System / United Kingdom	1. GUNT RT 5XX/6XX series, GERMANY / 2. EDIBON UCP series, SPAIN

No.	Item and Specifications	Units	Main Preference	Alternatives
4/5	Programmable Logic Controllers (PLC) Trainer Kit and Application Units, including: PLC circuit boards, I/O interfaces for progamming and applications, software and hardware simulation for REAL industrial applications such as conveyor belts, elevators, etc.	1 package (hardware and software) including some application units	FEEDBACK 34-500 series and 34-120 and 34-150 Systems / United Kingdom	1. GUNT RT 800 series, GERMANY / 2. EDIBON PLC-PI module and examples in Process Control Applications, SPAIN
5/5	Digital Storage Oscilloscope (minimum requirements): / Bandwidth 10 GHz or larger, Rise Time less than 100 ps, Sampling Rate 20 Giga-Samples per seconds or larger, at least 64 Mega-samples of data record per channel, USB port for a PC connection, necessary driver and softwares included.	3 (three) units	TEKTRONIX TDS 6000 series	Hewlett Packard (HP) or Agilent equivalent