1. Correct answers: +2 points, wrong answers: –1 points, no answer, no point:
We could see a SYSTEM as any process that ________________ an _____________ signal into an output signal. UNHAS is a SYSTEM with new __________________ as the input and the graduates as the output, while a rectifier is also a SYSTEM with an AC voltage as the input and ________________ as the output. Unwanted input signals are called _____________________, while unwanted output signals are called ___________________. SYSTEMs are represented by a mathematical tool called _____________________. A SYSTEM is said to be _____________________ if it has an inverse, but an _______________ is not an inverse of a rectifier, because a rectifier itself is a _____________________ system, shown by the fact that both +2 V and -2 V inputs have the same 2 V output.

2. Answer all questions on these sheets of paper, use the back side if necessary.

Calculate the output Y of system A, then determine the appropriate mathematical operation on system B to make it equivalent to the system A (10 points):

multiplier
Y
X
sistem A
-1
X = 0,25
Y

???

sistem B
-
-
-

Answer :

A system is represented by an input x(t) and output y(t) relation as follows: y(t) = -1 for x(t) > 0, dan y(t) = +1 for x(t) < 0. Is this system linear?

Answer (circle the correct answer): YES – NO (5 points)
    Proof: Input signals ------------------> Output Signals
    (fill in)	x1(t) = _______ ---------> y1(t) = _______
x2(t) = _______ ---------> y2(t) = _______
        1 = ____ 2 = _____ ---------> 1 y1(t) + 2 y2(t) = _______
x(t) = 1 x1(t) + 2 x2(t) = ______ –-------> y(t) = _______
Then_____________________________because____________________________________________________
_____________________________________________________________________________________(5 points)

Draw accurately the transfer characteristics of the above system on an X-Y axis (10 points)
Figure:

If x(t) is the input signal and y(t) is the output, is an amplitude modulator y(t) = x(t)[sin(100t)] a linear system? Answer the question first, then prove it!

Answer (cycle the correct answer): YES – NO (5 points)
 Bukti: Isyarat Masukan ------------------> Isyarat Luaran
    (fill up) for any x1(t) ---------> y1(t) = _______
        and x2(t) ---------> y2(t) = _______
        for any non-zero 1 dan 2 ---------> 1 y1(t) + 2 y2(t) = ____________
x(t) = 1 x1(t) + 2 x2(t) ---------> y(t) = _______________________________________________
        _______________________________________________
Then ______________________________________because___________________________________________
_____________________________________________________________________________________(5 points)

An RC PASSIVE FILTER is built as a circuit of 2 resistors and 1 capasitor, as follows:

C
R2
vi(t)

R1

Vi(s)
Vo(s)
G(s)

Vi(s) = vi(t)
Vo(s) = vo(t)
(a) If R1= 100 K C 10 F, and R2= 100 K, using the concept of impedancei, then determine G(s)= Vo(s)/Vi(s) ! (5 point)
(b) If vi(t) is a unit step function u(t), then determine vo(t), t > 0 ! (10 point)
(c) If vi(t) = 10sin(100t), a sinusoidal input, then determine vo(t) ! (10 point)
vo(t)
+

Answer:
{a}

The State Space Model of a system is represented by its block diagram:

Y2
U2
U1
Y1
X2
dt
dt
X1
X 2
X1

+
+
+
+
+
+
-
-

+

+

1. Determine the dimension of its A, B, C dan D matrices! (5 point)
2. Determine the state equation (5 point) and the output equation (5 point) while calculating the elements of A, B, C dan D matrices!

State Equation : x = Ax + Bu and
Output Equation : y = Cx + Du

Answer:
a.

2015