PART I (50 points): Complete the following sentences. 2 points for each right answer, -1 point for each wrong answer, zero for blanks of no answer.

An armature-controlled DC Motor can be modeled as a linear system with the armature voltage (Ea) as the input and __________________________() as the output. But, basically, an armature-controlled DC Motor is an electro-mechanical device that produces ___________(T) from the armature current (Ia) loop under constant magnetic field. One of the consequences of the linearity of a DC motor is the proportional relation between the ____________________ as the output with the _____________________ as the input. The proportional relationship is represented in a static model of the armature-controlled DC Motor: __________ with K= ______________________ Unfortunately, the static model only represents the motor's response in its _________________ state. The static model does not describe the _____________________ response of the motor. To look at the motor's transient response a ________________ model is needed. One of the dynamic models used in the classical control theory is called the __________________________ model, which is actually the system's _____________________ response. It is an urgency to control the DC Motor's __________________ surge during the motor's start and stop. From the simulation, it is clearly shown that the _____________________ surge in the transient state can be very large. In general, an armature-controlled DC Motor - especially in the speed control application - can be modeled as a _________________ order system. The most important parameters to characterize a second-order system are the _________________________() and the __________________________________________ (n), the later is of course different from the nominal angular velocity nom. An additional ______________ in series with the armature winding will increase and consequently will damp the response more. This additional resistor will reduce the ____________________ surge during the start, but also will make the nominal ______________________ unattainable. The nominal speed can be reached by slowly reducing the additional series resistor until _________. With the _______________-loop control, the surge current during start can be minimized effectively by slowly increasing the __________________________ up to its nominal value. To control the current surge during start can be done by applying the _____________-loop control system, which requires _____________________________ for feedbac.k. Besides, this control scheme is also designed to reduce the effects of the _____________________.

PART II(50 point): Jawablah dengan ringkas pada kertas ini juga (gunakan halaman di baliknya bila perlu).

A hypothetical armature-controlled DC Motor is modeled as a linear system with the transfer function shown in the following figure:

(s)
Eb(s)
Ea(s)
1,7

(0,005s + 0,02) (0,25s + 0,65)

1,8

+

-

Specify the motor parameters and complete the following table: (10 points):

Parameters	Symbols	Values	Units
	Ra	0,02
Arnature Inductance
Motor Constant
	J
	B
Generator Constant

Directly from the block-diagram, determine:

 Ia(s)
H(s) =
        Ea(s)

 (s)
G(s) =
        Ea(s)

(5 points) a.	(5 points) b.

From the above transfer functions, calculate the damping-ratio,  and the unndamped natural frequency, n in [rad/sec] of the motor model. (10 points):

If the nominal armature voltage Eanom is 500 Volt, determine the nominal armature current in Ampere and the nominal speed in RPM. (10 points)

An additional series resistor of 0,98 Ohm is installed, then determine damping ratio,  of the motor now and also its undamped natural frequency, n. Determine also its steady-state armature current in Ampere and its speed in RPM (10 points)