A Telemonitoring System for the Distribution Transformers of an Electrical Power Network: An Experiment to Measure the Inter-Node Delay

Abstract. A telemonitoring system is a necessity to maintain the quality of the service in a large electrical power network. In this research, a microcontroller-based telemonitoring system is designed for the distribution transformers, providing a data acquisition system to monitor 6 (six) power system parameters, including the three phase currents, two voltages and the temperature or the humidity in thousands of transformers in the area. The measurement is conducted using 6 (six) sensors installed in each one of the transformers as an outdoor unit along with the microcontroller and the network circuitry.. The outdoor unit is designed as a node of a large interconnected wifi network. This paper shows an experiment conducted to measure the delay between 2 (two) nodes in the network and its effects to the performance of the whole network. A prototype of an outdoor unit is connected in a mesh-topology with 2 (two) laptop computers, one is representing the server and the other is performing a neighboring node. The delay is tested for both single-hop and multi-hop data transmission configurations. In the multi-hop configuration, the delay is 785.97 miliseconds when the distance between two nodes is set to be 40 meters and in the single-hop configuration the delay is 803.05 miliseconds for a 31 meters of inter-node distance. This result proves that in a mesh-topology configuration the inter-node delay in the multi-hop configuration can be smaller than the delay in the single-hop configuration.